## Slide 1: Shale gas impacts on groundwater resources
Insights from monitoring a fracking site in Poland
Nelly Montcoudiol1 (Nelly.Montcoudiol@glasgow.ac.uk), Catherine Isherwood2, Andrew Gunning2, Thomas Kelly2, Paul Younger1
EGU – Vienna – 24th April 2017
1
2

## Slide 2: Introduction
Shale gas boom in the USA and controversy on environmental impacts of hydraulic fracturing (‘fracking’)
Cautious approach in Europe
SHale gas Exploration and Exploitation induced Risks
  Developing best practice to understand, prevent and mitigate the potential short- and long-term environmental impacts and risks from shale gas exploration and exploitation
Three major potential risks:
  Induced seismicity
  Groundwater contamination
  Air pollution

## Slide 3: Introduction
Hydraulic fracturing and possible scenarios of impact
d.) Abandoned well legacies – preferential pathways
Impacts on groundwater resources (modified after US EPA (2012))
US EPA (2012). Study of the Potential Impacts of Hydraulic Fracturing on Drinking Water Resources, PROGRESS REPORT, US Environmental Protection Agency Office of Research and Development Washington, DC, December 2012 EPA/601/R-12/011
Notes: At surface: abandoned well legacies, providing pathways from fracture stimulation zones to near surface GW
Around well-bore as result of failure in well integrity in which drilling fluids or flow back is allowed to escape in surrounding strata
Through GW flow arising from fracture stimulation

## Slide 4: Location of the drilling pad
Horizontal wells aligned with fault trends
Source: PGNiG
GW flow

## Slide 5: Chronology
Autumn 2015
Drilling of the horizontal wells
Installation of GW monitoring network
Dec. 2015 – May 2016
Baseline monitoring (6 months – 4 site visits)
June – July 2016
Fracking in the 2 horizontal wells
Sampling of GW, frac fluid and flowback fluid
Aug. 2016 - ….
On-going post-frac monitoring (visits every month in 2016, every 2 months in 2017)
2013
Drilling of the vertical well
Notes: Add pictures

## Slide 6: Data collection in the field
Continuous data
Site visits
Set up for groundwater sampling at well GW3
Pabs, TGW & Spec. Cond.
Patm, Tair
GW levels
Physico-chemical
parameters
Alkalinity
Samples for lab
analyses / QA
Ions
Metals
Dissolved gases
Isotopes

## Slide 7: Quaternary geology
Source: C. Isherwood
Notes: Semi-confined to confined/depth of wells

## Slide 8: Groundwater levels
Fracking
WYSIN-2
Fracking
WYSIN-3

## Slide 9: GW stable isotopes & recharge
H2O stable isotopes
  GW samples plot on the GMWL and interpolated LMWL
  Recharge in April and/or October
  Flowback fluid with different signature
Recharge model
  FAO (Allen et al. 1998)
  Composite model for soil occupation
    25% wheat
    25% Ray Grass
    20% wood
    15% pasture
    15% corn
Allen, R. G., L. S. Pereira, D. Raes & M. Smith, 1998. Crop evapotranspiration - Guidelines for computing crop water requirements-FAO Irrigation and drainage paper 56. FAO, Rome. 300(9): D05109.
Dry spring
Some recharge
Wet summer
Limited
recharge
Wet autumn
Recharge
(IAEA, 2016)
GMWL
IAEA, 2016. RCWIP (Regionalized Cluster-Based Water Isotope Prediction) Model – gridded precipitation δ18O|δ2H| δ18O and δ2H isoscape data. International Atomic Energy Agency. Vienna, Austria. From http://www.iaea.org/water, accessed April 2016.

## Slide 10: Temperature & specific conductivity
Temperature
Specific conductivity
Notes: Update figures (Matlab)

## Slide 11: Groundwater chemistry
Temporal variability
  During baseline
Groundwater
  Ca-HCO3
Flowback fluid
  Na-Cl
Frac fluid
  Na-HCO3?
5
5 meq/l
0
5
5 meq/l
0
1000
1000 meq/l
0
Ca
Mg
Na
Cl
HCO3
SO4
Scale 1:200
  During entire monitoring

## Slide 12: Conclusion & perspectives
Typical Quaternary aquifer
  Semi-confined to confined
  Limited variations of groundwater levels
  Recharge mainly occurring in Autumn
  Similar chemistry: Ca-HCO3 water type, with limited temporal variability
Signature of flowback fluid completely different
  No short-term impacts on GW resources from the exploration well / hydraulic fracturing
Statistics: are changes significant?
Groundwater model
  Aquifer behaviour
  Conditions for detecting impact

## Slide 13: Acknowledgement
This project has received funding from the EU’s Horizon 2020 research and innovation programme under grant number No 640896
  www.sheerproject.eu
Project partners
Notes: Logo of all partners